## Slide 1: Georeferencing Specimen Localities
Elizabeth Gjieli, Geographical Information Manager

## Slide 2: TABLE OF CONTENTS 1. Introduction & Mapping Tools 2. Methods & Protocols 3. Step-by-step Examples

## Slide 3: PART 1: INTRODUCTION & MAPPING TOOLS

## Slide 4: What is Georeferencing?
Interpreting a written description of a locality into mappable coordinates and an uncertainty radius in accordance with community best practices
Goals:
Find coordinates as accurately as possible
Calculate the smallest uncertainty radius that encapsulates entire area that the collection could have been within
Capture proper metadata so that georeferencing steps can be retraced and process is repeatable
Notes: What is georeferencing?

## Slide 5: Guides
We follow community agreed upon best practices for georeferencing, which include stepwise instructions based on categorization of the locality type
Georeferencing Quick Reference Guide (2020)
Georeferencing Quick Reference Guide (2012)
Best Practices Guide (2020)
Notes: What is georeferencing?

## Slide 6
To capture coordinates and uncertainty radii, we mainly use:
Google Maps
GEOLocate
Also may be used:
Google Earth
Bing Maps
ACME Mapper
GIS software
Mapping Tools

## Slide 7
Google Maps: Map Layers
selecting the scale bar toggles between units
Geo-tagged photos

## Slide 8
Terrain View

## Slide 9
Right click on a location to find coordinates
Capturing Coordinates
Coordinates are provided at top of menu – select to auto-copy. Or select “What’s here?” option to capture coordinates

## Slide 10
Right-click on the location, select
“Measure distance”
Measure Distance
Bonus: This tool also serves as a great way to pin a place on the map

## Slide 11
Left-click on the map to measure a linear segment. The nodes may be adjusted/deleted
Measuring Distance

## Slide 12
Radial
Measure Distance Tool is used to measure a feature’s radial
Radial

## Slide 13
http://museum.tulane.edu/geolocate/default.html
Works best for U.S., Canada, and Europe
GEOLocate
Automates georeferencing

## Slide 14
Pan around map
Zoom tool
Map scale
Country drop-down list
Locality search fields
Coordinates at cursor position
Full screen view
Base layer and overlay options
GEOLocate Web Application
GEOLocate

## Slide 15
Radial
Georeferenced point
GEOLocate Web Application

## Slide 16
Click “Resize uncertainty to polygon” to snap the radial to the region of the city (available when polygon of the feature is present)
Uncertainty: Automated

## Slide 17
Click “Edit uncertainty” to manually adjust the radial. This method is more time intensive.
Uncertainty: Manual
GEOLocate

## Slide 18
green dot =
best match
Offset at a Heading
20km N of Nantes, France

## Slide 19
Offset at a Heading
20km N
20km N of Nantes, France

## Slide 20
Reference Map Layers

## Slide 21
Translating Coordinate Systems
Geographic coordinates are sometimes provided on labels in various coordinate systems
Decimal degrees format is the most convenient for mapping and is the standard format we capture in EMu (e.g., 40.866680, -73.878735)
Coordinate systems can be converted between one another
More information on:
Township, Range, and Section (PLSS)
UTM coordinates

## Slide 22
Township-Range-Section Coordinate System (TRS)
  Example: T21N, R1W, S5 = Township 21 North / Range 1 West / Section 5
  State must be specified, and sometimes a meridian if a state has more than one
  Datum: NAD27
For U.S. locations only, mainly in the West, Midwest, and South
Useful tools to convert TRS to latitude and longitude coordinates: GEOLocate or TRS Conversion Calculator
Public Land Survey System (TRS)

## Slide 23
GEOLocate can translate TRS into decimal degrees if entered as: T(value direction) R(value direction) S(value), example: T37N R21W S14
GEOLocate to Convert TRS

## Slide 24
What is UTM?
Universal Transverse Mercator coordinate reference system
To use when coordinates provided on label in UTM format
UTM Calculator
Conversion Website
Notes: To convert UTM to latitude/longitude, use the RCN UTM Calculator

## Slide 25
Search fields
Lat/Long Coordinates
UTM Calculator
Conversion Website
Standard UTM coordinates
NATO/Military Grid Reference System UTM
Note: This information is captured in the Mapping Tab of the Sites Module in EMu
Notes: To convert UTM to latitude/longitude, use the RCN UTM Calculator

## Slide 26
  Historical places or ghost towns
  Remote areas
  Natural/geological features
  Spelling/translation variations
Example: Merced Falls, California
Often necessary to reference gazetteers or other sources
Digital Resources
present day
c.1900

## Slide 27
GeoNames: geographical database, crowdsourced
Wikimapia: online editable map, crowdsourced
OpenStreetMap: open geographic database updated and maintained by volunteers, crowdsourced
Mapcarta: an open map that uses data from OSM, Wikipedia, and other sources
Statoids: current/past administrative area names (generally up-to-date as of 2015)
Peakery: sometimes useful for mountains, crowdsourced
Traveling Luck: World Index, crowdsourced
Geographic Names Info. System (US data): maintains uniform geographic name usage U.S.
Getty Thesaurus of Geographic Names: a comprehensive vocabulary of place names
Falling Rain: Global Gazetteer
Digitized Perry-Castañeda Library (PCL) Map Collection digitized paper map collection
Also Google Web and Image Search and digitized historical maps
Digital Resources